## Slide 1: 武汉大学2019研究生入学考试考题
现有TCP拥塞窗口cwnd和传输轮次n的关系如表所示。解答以下问题：
（1）指出TCP在慢开始阶段的时间间隔（以轮次表示）（4分）
（2）指出TCP在拥塞避免阶段的时间间隔（以轮次表示）（4分）
（3）指出在第11轮次，门限ssthresh的值是多少？假设在第一轮次发送A的第一个报文段，指出A的第55个报文段在第几个轮次发送（4分）
n | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
cwnd | 1 | 2 | 4 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 4 | 6 | 7 | 8
(1) TCP在慢开始阶段的时间间隔: [1, 4]、[9, 12];
(2) TCP在拥塞避免阶段的时间间隔: [5, 8]、[13, 14];
(3) 阈值为6，第8轮次发送。
Review Problem

## Slide 2: 第四章 网络层: 数据平面
Slides are adapted from those of by J.F Kurose and K.W. Ross with copyright 1996-2020 J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: 第四章 网络层
本章目标:
揭示网络层服务背后的原理, 聚焦数据平面:
  网络层服务模型
  转发与路由
  路由器工作原理
  通用转发
实例化，在Internet上的实现
- 数据平面

## Slide 4
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
4.4 通用转发
第四章 网络层
- 数据平面
网络层 - 数据平面
Notes: SDN: software defined network

## Slide 5
4.1 网络层概述
  数据平面
  控制平面
4.2 路由器工作原理
4.3 IP: 网际协议
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 6: 网络层
将报文段从发送方传输到接收主机
在发送端将报文段封装到数据报中
在接收侧将数据报解码成报文段交付给传输层
网络层协议在每个主机、路由器内被实现
路由器检查通过它的所有IP数据报中的首部字段
4.1 Overview
网络层的
分组/包
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 7: 网络层的两个关键功能
网络层功能
转发：将分组从路由器的输入链路移动到适当的路由器输出链路
路由：决定分组从源到目标的路径
  路由算法
类比: 旅行
转发: 通过单个换乘的过程
路由: 对整个旅途从起点到目的地进行规划的过程
4.1 Overview

## Slide 8: 网络层: 数据平面、控制平面
数据平面
本地，单路由器功能
确定如何将到达路由器输入端口的数据报转发到路由器输出端口
转发功能
控制平面
网络全局逻辑
确定如何沿从源主机到目的主机的端到端路径在路由器之间路由数据报
两种控制平面方法:
  传统路由算法: 在路由器中实现
  软件定义网络(SDN): 在（远程）服务器中实现
1
2
3
0111
到达分组首部的值
4.1 Overview

## Slide 9
每路由器控制平面
路由
算法
数据
平面
控制
平面
1
2
0111
到达分组首部的值
3
4.1 Overview
每一路由器中各自的路由算法在控制平面中相互作用
决定端到端的路径
决定当前路由器如何转发

## Slide 10
数据
平面
控制
平面
逻辑集中控制平面
远程控制器
CA
CA
CA
CA
CA
1
2
0111
3
到达分组首部的值
4.1 Overview
独立（通常是远程）控制器与所有本地控制代理（CA）交互

## Slide 11: 网络服务模型
单个数据报的服务示例:
保证交付
保证交付，延迟不超过40毫秒
数据报流的服务示例:
数据报有序交付
保证最小流量带宽
对分组间隔变化的限制
4.1 Overview
4.1.2 Network service model
Q： 什么是"信道"为从发送方到接收方传输数据报提供的网络服务模型？
定义网络端到端之间的分组传输特性

## Slide 12: 网络服务模型
网络设施
互联网
ATM
ATM
ATM
ATM
服务
模型
尽力
而为
CBR
VBR
ABR
UBR
带宽
无
常速
速率
保证
最小
保证
无
丢失
无
有
有
无
无
顺序
无
有
有
有
有
时延
无
有
有
无
无
拥塞
反馈
无(通过
丢失推断)
无
拥塞
无
拥塞
有
无
保障 ?
4.1 Overview
4.1.2 Network service model
Asynchronous Transfer Mode
信元交换
Notes: ATM (Asynchronous Transfer Mode) : 异步传输模式，信元(cell)交换
未定比特速率（UBR：Unspecified Bit Rate）：对传输速率没有指定，但可靠性要求很高，即所谓"尽力传输"（Best Effort），用于局域网仿真（LAN Emulation）。
不变比特速率（CBR：Constant Bit Rate）：有固定的带宽（速率）要求，适用实时的话音和视频信号传输。
可用比特速率（ABR：Available Bit Rate）：只需指定峰值（Peak）和谷值（Minimum）信元速率，应用不多。
可变比特速率（VBR：Variable Bit Rate）：允许随时可变的带宽，但必须指定峰值带宽、最大突发数据长度和必须维持的最低速率。

## Slide 13
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 14
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 15: 路由器架构概述
高速
交换
结构
路由
处理器
路由器输入端口
路由器输出端口
转发数据平面
(硬件)以纳秒级
时间帧进行操作
路由、管理控制
平面(软件)以毫秒级
时间帧进行操作
high-level view of generic router architecture:
4.2 What's inside a router
分散式交换:
可以在每个输入端口
本地进行转发决策
通用路由器架构的总体视图
转发表
Notes: femtosecond: 飞秒 —— one quadrillionth, or one millionth of one billionth, of a second
picosecond: 皮秒 —— one trillionth, or one millionth of one millionth of a second
nanosecond：纳秒 —— one billionth of a second
microsecond: 微秒 —— one millionth of a second
millisecond: 毫秒 —— one thousandth of a second

## Slide 16: 输入端口功能
线路
终端
查找
转发
队列
分散交换 :
使用首部字段值，使用输入端口内存中的转发表查找输出端口（"匹配加动作"）
目标: 以'线速度'完成输入端口处理
排队：如果数据报到达的速度快于交换机构的转发速度
4.2 What's inside a router
4.2.1 Input Port Processing and Destination-Based Forwarding
链路层
协议
(接收)
交换
机构
物理层:
位级接收
数据链路层 :
例：以太网
参见第5章
Notes: line termination: 线路端接

## Slide 17: 输入端口功能
线路
终端
链路层
协议
(接收)
物理层:
位级接收
数据链路层 :
例：以太网
参见第5章
交换
机构
4.2 What's inside a router
4.2.1 Input Port Processing and Destination-Based Forwarding
查找
转发
队列
分散交换 :
使用首部字段值，使用输入端口内存中的转发表查找输出端口（"匹配加动作"）
基于目的地的转发：仅基于目的地IP地址转发（传统）
通用转发：基于任何一组首部字段值进行转发

## Slide 18: 基于目的地转发
目的地址范围
11001000 00010111 00010000 00000000
至
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
至
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
至
11001000 00010111 00011111 11111111
其它
链路接口
0
1
2
3
Q: 但如果范围划分得没这么好怎么办?
转发表
4.2 What's inside a router
4.2.1 Input Port Processing and Destination-Based Forwarding

## Slide 19: 最长前缀匹配
目的地址范围
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
其它
DA: 11001000 00010111 00011000 10101010
例子
DA: 11001000 00010111 00010110 10100001
哪个接口?
哪个接口?
用最长前缀匹配
链路接口
0
1
2
3
4.2 What's inside a router
在查找给定目的地址的转发表条目时使用与目的地址匹配的最长地址前缀
4.2.1 Input Port Processing and Destination-Based Forwarding

## Slide 20: 最长前缀匹配
稍后在讨论寻址时，我们将很快看到为何使用最长前缀匹配
最长前缀匹配：通常使用三态值内容寻址存储器（TCAM）执行
  内容可寻址: 向TCAM提供地址，不管表的大小在一个时钟周期内检索到地址
  Cisco Catalyst: TCAM中最多可以到~1M路由条目
4.2 What's inside a router
苏州雄立
4.2.1 Input Port Processing and Destination-Based Forwarding
光纤时代匹配速率非常重要！
Notes: 三态内容可寻址存储器(Tenary Content Address Memory)

## Slide 21: 交换机构
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
内存
memory
总线
纵横
交叉
4.2 What's inside a router
4.2.2 Switching
将分组从输入缓冲区传送到恰当的输出缓冲区
交换速率：分组从输入端传送到输出端的速率
  通常以输入/输出线速率的倍数来测量
  N输入：期待的交换速率是N乘以线速率
三种交换结构

## Slide 22: 经内存交换
第一代路由器:
由CPU直接控制交换的传统计算机
分组被拷贝到系统内存
速度受限于内存带宽 (每数据报 2 次总线跨越)
输入
端口
(例如
以太网)
内存
输出
端口
(例如
以太网)
系统总线
4.2 What's inside a router
4.2.2 Switching

## Slide 23: 经总线交换
数据报通过共享总线从输入端口存储器传到输出端口存储器
总线争用: 交换速度受总线带宽限制
32 Gbps 总线, Cisco 5600: 对接入和企业路由器来说速度足够
总线
4.2 What's inside a router
4.2.2 Switching
Notes: bus contention (总线竞争)

## Slide 24: 经互连线网络交换
克服总线带宽限制
榕树网络, 纵横交叉式, 其它最初为连接多处理器开发的互连线网络
高级设计 : 将数据报分割成固定长度的块，通过机构交换块
Cisco 12000系列: 通过互连线网络达到交换60Gbps
crossbar
纵横式/
交叉式
4.2 What's inside a router
4.2.2 Switching
interconnection net
（片内）互联线网络
Notes: banyan network 榕树网

## Slide 25: 输入端口排队
交换机构比输入端口叠加的速度慢->输入队列中可能出现排队
  输入缓冲溢出导致队列时延和分组丢失!
队首(HOL, Head-of-the-Line )阻塞 : 队列前部的排队数据报阻塞了队列中其它数据报的转发
输出端口争用:
只能传输一个红色数据报. 下方的红色分组被阻塞
交换
机构
一次分组转发后: 绿色分组将经历 HOL 阻塞
交换
机构
4.2 What's inside a router
4.2.4 Where Does Queuing Occur?

## Slide 26: 输出端口
当数据报从交换机构中以高于传输速率的速度到达时需要缓冲
调度规则在队列中选择数据报进行传输
线路
端接
链路层
协议
（发送）
交换
机构
数据报
缓冲区
排队
这张幻灯片非常重要!
优先级调度 – 谁获得最佳性能，网络中立性
4.2 What's inside a router
4.2.4 Where Does Queuing Occur?
数据报（分组）可能由于拥塞、缺少缓冲而丢失

## Slide 27: 输出端口排队
通过交换机的到达率超过输出线速时进行缓冲
排队(延迟)和输出端口缓冲区溢出造成的丢失！
在时刻 t, 由输入到输出的分组增多
一个分组之后
交换
机构
交换
机构
4.2 What's inside a router
4.2.4 Where Does Queuing Occur?

## Slide 28: 需要多少缓存 ?
RFC 3439 经验法则：平均缓存等于"典型"RTT（比如250毫秒）乘以链路容量 C
  例如, C = 10 Gpbs 链路: 2.5 Gb 缓冲
最近的建议：在 N 条 TCP 流的情况下，所需缓冲数量
4.2 What's inside a router
4.2.4 Where Does Queuing Occur?

## Slide 29: 调度机制
调度: 选择要在链路上发送的下一个分组
FIFO (先进先出) 调度: 按到达队列的顺序发送
  现实世界的例子?
  丢弃策略：如果分组到达满员队列：丢弃谁?
    弃尾: 丢弃刚到达的分组
    优先级: 基于优先级丢弃/删除
    随机: 随机丢弃/删除
队列
（等候区）
分组
到达
分组
离开
链路
（服务器）
4.2 What's inside a router
4.2.5 Packet Scheduling

## Slide 30: 调度策略：优先级
优先级调度: 发送高优先级队列中的分组
多类别, 带不同优先级
  类别可能依赖于标记或其它首部信息，例如IP源/目标、端口号等
  真实世界举例?
高优先级队列
(等候区)
低优先级队列
(等候区)
到达
分类
离开
链路
(服务器)
1
3
2
4
5
5
5
2
2
1
1
3
3
4
4
到达
离开
服务中
的
分组
4.2 What's inside a router
4.2.5 Packet Scheduling

## Slide 31: 调度策略：更多
循环(Round Robin) 调度:
多类别
循环扫描分类队列，从每个类别发送一个完整的分组（如果可用）
1
2
3
4
5
5
5
2
3
1
1
3
2
4
4
到达
离开
服务中
的
分组
4.2 What's inside a router
4.2.5 Packet Scheduling

## Slide 32: 调度策略：更多
加权公平排队（WFQ）:
推广的循环
每个类别在每个周期中获得加权服务量
4.2 What's inside a router
4.2.5 Packet Scheduling
分类
到达
离开
链路
Notes: 加权公平队列

## Slide 33
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 34
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 35
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 36
TELNET
HTTP
FTP
SMTP
DNS
RIP
SNMP
DHCP
TCP
UDP
IP
ICMP
OSPF
ARP
RARP
application layer
transport
layer
network
layer
The Internet Hourglass
link
layer
ethernet
802.11
SONET
ATM

## Slide 37: The Internet 网络层
forwarding
table
host, router 网络层 functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router "signaling"
transport layer: TCP, UDP
link layer
physical layer
network
layer
4.3 IP: Internet Protocol

## Slide 38: IPv4 datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
"type" of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead
4.3 IP: Internet Protocol
4.3.1 IPv4 Datagram Format
measured in units of eight-byte blocks

## Slide 39: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided ("fragmented") within net
  one datagram becomes several datagrams
  "reassembled" only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
4.3 IP: Internet Protocol
4.3.2 IPv4 Datagram Fragmentation

## Slide 40: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
4.3 IP: Internet Protocol
4.3.2 IPv4 Datagram Fragmentation

## Slide 41
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 42
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 43: IPv4 addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router's typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 44: IPv4 addressing: introduction
Q: how are interfaces actually connected?
A: we'll learn about that in chapter 5, 6.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don't need to worry about how one interface is connected to another (with no intervening router)
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 45: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what's a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 46: Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 47: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 48: IPv4 addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
prefix
dotted-decimal form
Notes: 无类别域间路由 CIDR

## Slide 49: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from a DHCP server
  "plug-and-play"
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 50: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/"on")
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts "DHCP discover" msg [optional]
  DHCP server responds with "DHCP offer" msg [optional]
  host requests IP address: "DHCP request" msg
  DHCP server sends address: "DHCP ack" msg
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 51: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 52: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I'm a DHCP server! Here's an IP address you can use
Broadcast: OK. I'll take that IP address!
Broadcast: OK. You've got that IP address!
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 53: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 54: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 55: DHCP: example
DHCP server formulates DHCP ACK containing client's IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 56: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 57: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP's address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
Internet Corporation for Assigned Names and Numbers (ICANN)

## Slide 58: Hierarchical addressing: route aggregation
"Send me anything
with addresses
beginning
200.23.16.0/20"
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
"Send me anything
with addresses
beginning
199.31.0.0/16"
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
Notes: 路由聚合
路由摘要（route summarization）
Fly by night: 不可信

## Slide 59: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
"Send me anything
with addresses
beginning
200.23.16.0/20"
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
"Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23"
200.23.20.0/23
Organization 2
.
.
.
.
.
.
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing
longest prefix matching

## Slide 60: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
    allocates addresses
    manages DNS
    assigns domain names, resolves disputes
4.3 IP: Internet Protocol
4.3.3 IPv4 Addressing

## Slide 61: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)
Notes: 网络地址转换

## Slide 62: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
    range of addresses not needed from ISP: just one IP address for all devices
    can change addresses of devices in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    devices inside local net not explicitly addressable, visible by outside world (a security plus)
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)

## Slide 63: NAT: network address translation
implementation: NAT router must:
    outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
    remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
    incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)

## Slide 64: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)

## Slide 65: NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  address shortage should be solved by IPv6
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  NAT traversal: what if client wants to connect to server behind NAT?
4.3 IP: Internet Protocol
4.3.4 Network Address Translation (NAT)
Notes: NAT 穿透

## Slide 66
4.1 网络层概述
  data plane
  control plane
4.2 路由器工作原理
4.3 IP: 网际协议
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 通用转发 and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
第四章: outline
4.3 IP: Internet Protocol

## Slide 67
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 68
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 69: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed
4.3 IP: Internet Protocol
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)

## Slide 70: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same "flow."
(concept of "flow" not well defined).
next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
4.3 IP: Internet Protocol
traffic class

## Slide 71: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by "Next Header" field
ICMPv6: new version of ICMP
  additional message types, e.g. "Packet Too Big"
  multicast group management functions
4.3 IP: Internet Protocol

## Slide 72: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no "flag days"
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
4.3 IP: Internet Protocol

## Slide 73: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
4.3 IP: Internet Protocol

## Slide 74: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4
4.3 IP: Internet Protocol

## Slide 75: IPv6: adoption
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  20 years and counting!
  think of application-level changes in last 20 years: WWW, Facebook, streaming media, Skype, …
  Why?
4.3 IP: Internet Protocol
《推进互联网协议第六版(IPv6)规模部署行动计划》
http://www.gov.cn/zhengce/2017-11/26/content_5242389.htm

## Slide 76
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
4.4 通用转发
第四章 网络层
网络层 - 数据平面
- 数据平面
Notes: SDN: software defined network

## Slide 77
4.1 网络层概述
4.2 路由器工作原理
4.3 IP: 网际协议
4.4 通用转发
  match
  action
  OpenFlow examples of match-plus-action in action
第四章 网络层
网络层 - 数据平面
https://www.sdnctc.com/
- 数据平面
Notes: SDN: software defined network

## Slide 78
通用转发与 SDN
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each router contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions
4.4 Generalized Forward and SDN

## Slide 79: OpenFlow data plane abstraction
flow: defined by header fields
通用转发: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
Flow table in a router (computed and distributed by controller) define router’s match+action rules
4.4 Generalized Forward and SDN

## Slide 80: OpenFlow data plane abstraction
flow: defined by header fields
通用转发: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard
4.4 Generalized Forward and SDN

## Slide 81: OpenFlow: Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
网络层
Transport layer
4.4 Generalized Forward and SDN
Notes: Now I’ll describe the API that tries to meet these goals.
81

## Slide 82
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
Examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward (block) all datagrams sent by host 128.119.1.1
4.4 Generalized Forward and SDN
Notes: Port 22: ssh

## Slide 83
Destination-based layer 2 (switch) forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
port3
Examples
layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to output port 6
22:A7:23:
11:E1:02
4.4 Generalized Forward and SDN

## Slide 84: OpenFlow abstraction
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: unifies different kinds of devices
4.4 Generalized Forward and SDN
≈ broadcast
Notes: flood: 广播

## Slide 85: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2
4.4 Generalized Forward and SDN

## Slide 86
网络层概述:
  data plane
  control plane
路由器工作原理
IP: 网际协议
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
第四章 summary
通用转发 and SDN
  match plus action
  OpenFlow example
网络层 - 数据平面

## Slide 87: Homework
选做5道
网络层 - 数据平面