## Slide 1: 第六章 链路层和局域网
Slides are adapted from those of by J.F Kurose and K.W. Ross with copyright 1996-2020 J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: 第六章 链路层和局域网
本章教学目标:
链路层服务背后的原理
  错误检测、修正
  共享广播信道: 多路访问(接入)
  链路层寻址
  局域网: 以太网, VLAN
不同链路层技术的实例化、实现
链路层与局域网

## Slide 3: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 4: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 5: 链路层: 介绍
术语:
主机与路由器: 节点
沿通信路径连接相邻节点的通信信道: 链路
  有线链路
  无线链路
  局域网
第2层的分组(包): 帧, 封装数据报
数据链路层职责是从一个节点传输
数据报到链路上 物理相邻 的节点
6.1 introduction, services

## Slide 6: 链路层: 背景
采用不同的链路协议通过不同链路来传输的数据报:
  例如 第一条链路为以太网，中间链路上是帧中继，最后一个链路上则是 802.11
每种链路协议提供不同的服务
  例如 链路上提供还是不提供 rdt 服务
交通类比:
从武汉大学到斯坦福的旅程
  豪车: 武大校园至 WUH
  飞机: WUH 到 SFO
  caltrain: SFO 到 Palo Alto
游客 = 数据报
交通分段 = 通信链路
运输形式 = 链路层协议
旅行社 = 路由算法
6.1 introduction, services

## Slide 7: 链路层服务
成帧、链路访问:
  将数据报封装到帧中，添加首、尾
  共享媒介时的信道访问
  帧首部中的 "MAC" 地址用于标识源、目标
    不同于 IP 地址!
相邻节点间的可靠传输
  我们已经学过如何做 (第 3 章)!
  极少用于低比特差错链路 (光纤、一些双绞线)
  无线链路: 高错误率
    Q: 为何既要链路级也要端到端的可靠性?
6.1 introduction, services

## Slide 8: 链路层服务 (更多)
流控制:
  在相邻发送与接收节点间的速度控制
差错检测:
  信号衰减、噪声引起的差错
  接收方检测到错误的存在:
    通知发送方重传或丢弃帧
错误修正:
  接收器识别并校正位错误而不诉诸重传
半双工与全双工
  对于半双工，链路两端的节点可以传输但不能同时传输
6.1 introduction, services

## Slide 9: 链接层在哪里实现 ?
在每一主机内
链路层实现在 "适配器" 内(亦称 network interface card NIC) 或 芯片上
  以太网卡、802.11 卡; 以太网芯片组
  实现链路、物理层
连接到主机的系统总线
硬件、软件、固件的组合
controller
physical
transmission
cpu
memory
主机总线
(例如 PCI)
network adapter
card
application
transport
network
link
link
physical
6.1 introduction, services

## Slide 10: 适配器通信
发送侧:
  将数据报封装到帧中
  添加错误校验、rdt、流控制等
接收侧:
  查找错误、rdt、流控制等
  提取数据报、传送到接收方的上层
控制器
控制器
发送方主机
接收方主机
数据报
数据报
数据报
帧
6.1 introduction, services

## Slide 11: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 12: 错误检测
EDC = Error Detection and Correction bits (冗余)
D = 受错误检查保护的数据，可能包括首部字段
差错检测非 100% 可靠!
  协议可能会遗漏一些错误, 但罕见
  越大的 EDC 字段产生的检测与校正错误效果越好
otherwise
6.2 error detection, correction

## Slide 13: 奇偶校验
单校验位:
检测单个位错误
0
0
6.2 error detection, correction
二维奇偶校验
检测并修正单个位错误

## Slide 14: 互联网校验和 (回顾)
发送方:
将报文段内容视为16位整数序列
校验和: 报文段内容的和 (1 的补码和)
发送方将校验和的值放入 UDP 校验和字段
接收方:
计算收到的报文段的校验和
检查计算出的校验和是否等于校验和字段值
  否: 检测到错误
  是: 未检测到错误。但错误可能依然存在?
目的: 检测传输分组中的 "错误" (例如位翻转) (注: 仅用于传输层)
6.2 error detection, correction

## Slide 15: 循环冗余校验
更强大的差错检测编码
将 d 比特数据 D 视作二进制数
选择 r+1 位模板 (生成器) G
目标: 选择 r CRC 位 R, 使得
  <D,R> 完全被 G 整除 (模 2)
  接收方知道 G, 将 <D, R> 除以 G. 如果余数非零：检测到错误!
  可以检测所有少于 r+1 位的突发错误
广泛应用于实践 (以太网, 802.11 WiFi, ATM)
6.2 error detection, correction
目标: 选择 r 位 R, 使得

## Slide 16: CRC 例子
想要:
  D . 2r XOR R = nG
等价于:
  D . 2r = nG XOR R
等价于:
如果我们把 D . 2r 除以 G, 需要余数 R 满足:
1 0 1 0 1 1
1 0 0 1 √ 1 0 1 1 1 0 0 0 0
1 0 0 1
1 0 1
0 0 0
1 0 1 0
1 0 0 1
1 1 0
0 0 0
1 1 0 0
1 0 0 1
0 1 1
R = remainder [ ]
D.2r
G
6.2 error detection, correction
G
R
D

## Slide 17: 循环冗余校验
强大的错误检测方案
使用二进制除法而不是加法  有限代数理论(Galois 域)
可以用少量硬件轻松实现
  移位寄存器
  XOR (对加法和减法)

## Slide 18: 二进编码序列可以看作是二进多项式
或
可以看作
1
1
1
1
0
0
0
课外阅读材料

## Slide 19: 乘法
1
1
1
1
0
0
0
0
0
0
课外阅读材料

## Slide 20: 乘法
1
0
1
1
0
0
1
1
1
0
课外阅读材料

## Slide 21: 加法
课外阅读材料

## Slide 22: 循环冗余校验
假设有 k 比特报文和 n 位冗余
将比特与一多项式系数相关联 1 0 1 1 0 1 1 1x6 + 0x5+ 1x4+ 1x3 + 0x2 +1x+1 = x6 + x4 + x3 + x + 1
xxxxxxxxxx yyyy
k 比特
n 比特
长度 k + n 的块
课外阅读材料

## Slide 23: 循环冗余校验
设 M(x) 为 信息多项式
设 G(x) 为 生成多项式
  对给定的 CRC 方案 G(x) 是固定的
  G(x) 被发送方和接收方都知晓
基于 M(x) 与 G(x) 创建 码元多项式 C(x) 使得 C(x) 可被 G(x) 整除
课外阅读材料

## Slide 24: 循环冗余校验
发送方
  将 M(x) 乘以 xn
  将 xnM(x) 除以 G(x)
  忽略商并保留余数 R(x)
  形成并发送 C(x) = xnM(x)+R(x)
接收方
  接收到 C'(x)
  将 C'(x) 除以 G(x)
  如果余数为 0 则接收, 否则拒绝
课外阅读材料

## Slide 25: CRC 生成证明
余数 0
余数 0
注记: 模 2 加法与模 2 减法是等价的  R(x) + R(x) = 0
课外阅读材料

## Slide 26: 例
发送方
  M(x) = 110011  x5+x4+x+1 (6 bits)
  G(x) = 11001  x4+x3+1 (5 bits, n = 4)  4 bits of redundancy
  Form xnM(x)  110011 0000  x9+x8+x5+x4
  Divide xnM(x) by G(x) to find R(x)
= R(x)
Send the block 110011 1001
接收方
No remainder
 Accept
课外阅读材料

## Slide 27: CRC 的性质
Sent C(x), but received C'(x) = C(x)+E(x) When will E(x)/G(x) have no remainder, i.e., when does CRC fail to catch an error?
Single Bit Error  E(x) = xi If G(x) has two or more terms, G(x) will not divide E(x)
2 Isolated Single Bit Errors (double errors) E(x) = xi+xj, i > j E(x) = xj (xi-j + 1) Provided that G(x) is not divisible by x, a sufficient condition to detect all double errors is that G(x) does not divide (xt + 1) for any t up to i-j (i.e., block length)
课外阅读材料

## Slide 28: CRC 的性质
Odd Number of Bit Errors If x+1 is a factor of G(x), all odd number of bit errors are detected Proof: Assume an odd number of errors has x+1 as a factor. Then E(x) = (x+1)T(x). Evaluate E(x) for x = 1  E(x) = E(1) = 1 since there are odd number of terms (x+1) = (1+1) = 0 (x+1)T(x) = (1+1)T(1) = 0  E(x) ≠ (x+1)T(x)
课外阅读材料

## Slide 29: CRC 的性质
Short Burst Errors (Length t ≤ n, number of redundant bits) E(x) = xj(xt-1+…+1)  Length t, starting at bit position j If G(x) has an x0 term and t ≤ n, G(x) will not divide E(x) All errors up to length n are detected
Long Burst Errors (Length t = n+1) Undetectable only if burst error is the same as G(x) G(x) = xn + … + 1 n -1 bits between xn and x0 E(x) = 1 + … + 1 must match Probability of not detecting the error is 2-(n-1)
Longer Burst Errors (Length t > n+1) Probability of not detecting the error is 2-n
课外阅读材料

## Slide 30: CRC 的性质
Example:
  CRC-12 = x12+x11+x3+x2+x+1 CRC-16 = x16+x15+x2+1 CRC-CCITT = x16+x12+x5+1
  CRC-16 and CRC-CCITT catch all
    Single and double errors
    Odd number of bit errors
    Bursts of length 16 or less
    99.997% of 17-bit error bursts
    99.998% of 18-bit and longer error bursts
课外阅读材料

## Slide 31: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 32: 多路访问链路、协议
两种类型的 "链路":
点对点
  PPP 拨号接入
  以太网交换机与主机之间的点对点链路
广播 (共享线路或媒介)
  老式以太网
  上行 HFC
  802.11 无线 LAN
有线共享 (例如
电缆以太网)
共享 RF
(例如 802.11 WiFi)
共享 RF
(卫星)
鸡尾酒会上的人们
(共享空气、声学)
6.3 multiple access protocols
Notes: hybrid fiber-coaxial cable

## Slide 33: 多路访问协议
单一共享广播信道
两个或多个节点同时传输: 干扰
  当节点同时接收到两个或多个信号时发生冲突
多路访问协议
确定节点如何共享信道的分布式算法，即确定节点何时可以传输
有关信道共享的通信必须使用信道本身!
  无带外协调信道
6.3 multiple access protocols

## Slide 34: 理想的多路访问协议
给定: 速率 R bps的广播信道
欲求:
  1. 当一个节点要传输时, 它以速率 R 发送
  2. 当 M 个节点要传输时, 每个以平均速率 R/M 发送
  3. 完全分散:
    没有特殊节点来协调传输
    时钟、时隙不同步
  4. 简单
6.3 multiple access protocols

## Slide 35: MAC 协议: 分类
三种概括类型:
信道划分
  将信道划分为小的 "片段" (时隙, 频率, 码)
  将片段分配给节点独占使用
随机接入
  不分割信道，允许冲突/碰撞
  冲突后的"恢复"
"轮流"
  节点轮流发送，但发送多的节点可以轮流发送更长的时间
6.3 multiple access protocols

## Slide 36: 信道划分 MAC 协议: TDMA
TDMA: time division multiple access(时分多址)
信道的访问方式为 "回合"
每一站在每一轮中获得固定长度的时隙 (长度 = 分组传输时间)
未使用的时隙将空闲
例: 6 站 LAN, 1,3,4 有分组发送, 时隙 2,5,6 空闲
1
3
4
1
3
4
6 时隙
帧
6 时隙
帧
6.3 multiple access protocols

## Slide 37: 信道划分 MAC 协议: FDMA
FDMA: frequency division multiple access (频分多址)
信道频谱划分成频带
每站分配固定频段
频带中未使用的传输时间成为空闲
例: 6 站 LAN, 1,3,4 有分组要发送, 频带 2,5,6 空闲
频带
时间
FDM 电缆
6.3 multiple access protocols

## Slide 38: 随机接入协议
当节点要发送分组时
  以信道数据全速率 R 传输
  节点间无 先期 协调
两个或多个传输节点 ➜ "冲突",
随机接入 MAC 协议 规范:
  如何检测碰撞/冲突
  如何从冲突中恢复(例如 通过延迟重传)
随机接入 MAC 协议的例子:
  时隙 ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA
6.3 multiple access protocols

## Slide 39: 时隙 ALOHA
假设:
所有帧大小相同
时间划分为相同大小的时隙 (传输 1 帧的时间)
只在时隙开启后节点开始传输
节点被同步
如果两个或多个节点在时隙中传输，则所有节点都检测到冲突
操作:
当节点获得新帧时，在下一时隙中传输
  如果无冲突: 节点可在下一个时隙中发送新帧
  如果冲突: 节点以概率 p 在每个后续时隙中重新传输该帧直到成功
6.3 multiple access protocols

## Slide 40: 时隙 ALOHA
优势:
单个活动节点可以以信道的全速率连续传输
高度分散: 仅节点中的时隙需要同步
简单
缺陷:
冲突, 时隙浪费
空闲时隙
节点可以在不到发送完分组所需时间内检测到冲突
时钟同步
1
1
1
1
2
3
2
2
3
3
节点 1
节点 2
节点 3
C
C
C
S
S
S
E
E
E
6.3 multiple access protocols
Notes: Pros 利
Cons 弊
pros and cons 利弊

## Slide 41: 时隙 ALOHA: 效率
假设: N 个节点有许多帧要发送, 每个在时隙进行传输的概率为 p
给定节点在某个时隙成功的概率 = p(1-p)N-1
有一节点成功的概率 = Np(1-p)N-1
最大效率: 找到 p* 使得 Np(1-p)N-1 最大
对众多节点, 取 N 趋向无穷大时 Np*(1-p*)N-1 的极限得到:
最大效率 = 1/e = .37
效率: 长时运行情况下成功时隙的占比 (多节点、多帧需要发送)
最佳: 有效传输占信道使用时长为37%
!
6.3 multiple access protocols

## Slide 42: 纯 (非时隙) ALOHA
非时隙 Aloha: 简单、无同步
当帧首次到达
  立刻传输
冲突概率增加:
  t0 时刻发送的帧与其它在 [t0-1,t0+1] 时段发送的帧冲突
6.3 multiple access protocols

## Slide 43: 纯 ALOHA 效率
P(给定节点成功) = P(节点传输) .
P(无其它节点在 [t0-1,t0] 传输) .
P(无其它节点在 [t0-1,t0] 传输)
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… 选择最佳 p 并令 N
= 1/(2e) = .18
比时隙 Aloha 更糟 !
6.3 multiple access protocols

## Slide 44: CSMA (载波侦听多路访问)
CSMA: 传输前侦听:
如果检测到信道闲, 发送整个帧
如果检测到信道忙, 推迟传输
人类类比: 不要打断别人!
6.3 multiple access protocols
Notes: 载波侦听多路访问

## Slide 45: CSMA 冲突
冲突依然可能发生: 传播时延意味着两个节点可能没听到对方传输
冲突: 整个分组传输时间被浪费
  距离与传播时延在确定冲突概率中起作用
节点的空间布局
6.3 multiple access protocols

## Slide 46: CSMA/CD (冲突检测)
CSMA/CD: 载波侦听、延迟如同 CSMA
  短时间内检测到冲突
  冲突的传输被终止, 减少信道的浪费
冲突检测:
  有线局域网中容易: 测量信号强度，比较发送和接收信号
  无线局域网中难: 接收信号强度受本地传输强度的覆盖
人类类比: 礼貌的健谈者
6.3 multiple access protocols
Notes: 冲突检测

## Slide 47: CSMA/CD (冲突检测)
节点的空间布局
6.3 multiple access protocols

## Slide 48: 以太网 CSMA/CD 算法
1. 网卡从网络层接收数据报, 创建帧
2. 如果 NIC 检测到信道闲，则启动帧传输; 如果NIC检测到信道忙, 则等待直到信道空闲，然后传输
3. 如果 NIC 在没有检测到其它传输的情况下传输完整个帧，则 NIC 完成该帧 !
4. 如果网卡在传输时检测到其它传输，则中止并发送干扰信号
5. 中止后，NIC 进入二进(指数)退避:
  在 m 次碰撞后, NIC 从 { 0, 1, 2, …, 2m - 1 } 中随机选择 K . NIC 等待 K·512 比特时间, 返回到步骤 2, m 最大为 10
  更多的碰撞意味着更长的退避间隔
6.3 multiple access protocols
Notes: truncated binary exponential backoff: 截断二进指数退避
NIC = Net Interface Card

## Slide 49: CSMA/CD 效率
Tprop = LAN 中两个节点间最大传播时延
ttrans = 传输最大帧的时间
6.3 multiple access protocols
efficiency 趋近 1
  当 tprop 趋向 0
  当 ttrans 趋向无穷大
比 ALOHA 更好的性能: 且简单、便宜、分散!

## Slide 50: "轮流" MAC 协议
信道划分 MAC 协议:
    高负载下高效公平地共享信道
    低负载时效率低下: 信道访问延迟, 即使只有一个活跃节点也仅分配 1/N 带宽!
随机接入 MAC 协议
    低负载时效率好: 单节点可完全利用信道
    高负载: 冲突开销
"轮流" 协议
  两种世界中寻找最好!
6.3 multiple access protocols
Notes: overhead: 开销, 费用

## Slide 51: "轮流" MAC 协议
轮询:
主节点"邀请"从节点轮流发送
通常带 "哑" 从设备一起使用
考虑:
  轮询开销
  延迟
  单点故障 (主)
master
slaves
poll
data
data
6.3 multiple access protocols

## Slide 52: "轮流" MAC 协议
令牌传递:
控制令牌按顺序从一个节点传递到下一个节点
令牌消息
考虑:
  令牌开销
  延迟
  单点故障 (令牌)
T
data
(无需发送)
T
6.3 multiple access protocols

## Slide 53: 有线接入网
cable headend
CMTS
ISP
cable modem
termination system
cable
modem
splitter
…
…
Internet frames, TV channels, control transmitted
downstream at different frequencies
upstream Internet frames, TV control, transmitted
upstream at different frequencies in time slots
6.3 multiple access protocols
多个 40Mbps 下行 (广播) 信道
  单 CMTS 传输到信道
多个 30 Mbps 上行信道
  多路访问: 所有用户争用某些上行信道时隙 (其它已被分配)

## Slide 54: 有线接入网
MAP frame for
Interval [t1, t2]
Residences with cable modems
Downstream channel i
Upstream channel j
t1
t2
Assigned minislots containing cable modem
upstream data frames
Minislots containing
minislots request frames
cable headend
CMTS
6.3 multiple access protocols
DOCSIS: data over cable service interface spec(有线数据服务接口规范)
上行、下行频率信道 FDM
上行 TDM: 一些时隙被分配，一些有争用
  下行 MAP 帧: 指定上行时隙
  请求上行时隙 (及数据) 在选定的时隙中随机接入传输 (二进退避)
Notes: truncated binary exponential backoff: 截断二进制指数退避

## Slide 55: MAC 协议总结
信道划分, 按时间、频率或编码
  时分、频分
随机接入 (动态),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  载波侦听: 在某些技术中(有线)容易, 某些中 (无线)难
  CSMA/CD 用于以太网
  CSMA/CA 用于 802.11
轮流
  由中心站轮询、令牌传递
  蓝牙、FDDI、令牌环
6.3 multiple access protocols
Notes: the fiber distributed data interface (FDDI)
CSMA/CA(Carrier Sense Multiple Access with Collision Avoidance)：带有冲突避免的载波监听多路访问

## Slide 56: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 57: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
  寻址、ARP
  以太网
  交换机
  VLAN
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 58: MAC 地址与 ARP
32 位 IP 地址:
  接口的网络层地址
  用于第3层 (网络层) 转发
MAC (或 LAN 或 物理 或 以太网) 地址:
  功能: "本地" 使用的从一个接口到另一个物理相连接的接口获取帧 (同一网络, 在 IP 地址意义下)
  48 位 MAC 地址 (对于大多数局域网) 在 NIC ROM 中烧录, 有时也可以通过软件设置
  例如: 1A-2F-BB-76-09-AD
16 进制 (基数 16) 表示法
(每一 "数字" 代表 4 比特)
6.4 局域网

## Slide 59: LAN 地址与 ARP
局域网上的每个适配器都有唯一的局域网地址
适配器
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)
6.4 局域网

## Slide 60: LAN 地址 (更多)
MAC 地址分配由 IEEE 管理
制造商购买 MAC 地址空间块 (以确保唯一性)
类比:
  MAC 地址: 如同身份证号
  IP 地址: 如同邮政地址、邮编
MAC 扁平地址 ➜ 可移动
  可以将LAN卡从一个LAN移动到另一个LAN
IP 分层地址不可移动
  地址取决于连接到哪个节点的IP子网
6.4 局域网

## Slide 61: ARP: 地址解析协议
ARP 表: 局域网上的每个 IP 节点(主机、路由器)都有表
  某些 LAN 节点的 IP/MAC 地址映射:
< IP 地址; MAC 地址; TTL>
  TTL (Time To Live): 此段时间之后该地址映射将被撤销 (通常 20 分钟)
问题: 在知道 IP 地址时, 如何确定接口的MAC地址?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
6.4 局域网
Notes: address resolution protocol

## Slide 62: ARP 协议: 同一 LAN
A 要向 B 发送数据报
  B 的 MAC 地址不在 A 的 ARP 表中
A 广播 ARP 查询分组, 含有 B 的 IP 地址
  目标 MAC 地址 = FF-FF-FF-FF-FF-FF
  局域网上所有节点收到 ARP 查询
B 收到 ARP 分组, 将其(B 的) MAC 地址回复给 A
  发送给 A 的 MAC 地址的帧 (单播)
A 缓存 (保存) IP 到 MAC 地址对到其 ARP 表中直到信息过时 (超期)
  软状态: 除非刷新，否则超时(消失)的信息
ARP 是 "即插即用":
  节点在无需网络管理员干预的情况下创建其 ARP 表
6.4 局域网

## Slide 63: The Internet Hourglass
TELNET
HTTP
FTP
SMTP
DNS
RIP
SNMP
DHCP
TCP
UDP
IP
ICMP
OSPF
ARP
RARP
application layer
transport
layer
network
layer
link
layer
ethernet
802.11
SONET
ATM
6.4 局域网

## Slide 64: 寻址: 路由到另一 LAN
排演: 自 A 通过 R 发送数据报到 B
  专注于寻址 – IP (数据报) 及 MAC 层 (帧)
  假设 A 知道 B 的 IP 地址
  假设 A 知道第一跳路由器 R 的 IP 地址 (how?)
  假设 A 知道 R 的 MAC 地址 (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
6.4 局域网

## Slide 65: 寻址: 路由到另一 LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
  A 使用 IP 源为 A 和目标为 B 创建 IP 数据报
  A 创建以 R 的 MAC 地址为目标地址的链路层帧，帧包含 A 到 B的 IP 数据报
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
6.4 局域网

## Slide 66: 寻址: 路由到另一 LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
  帧自 A 发送到 R
IP
Eth
Phy
  帧在 R 收到, 数据报移除, 传递给 IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222
6.4 局域网

## Slide 67: 寻址: 路由到另一 LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
  R 转发 IP 源 A，目标 B 的数据报
  R 创建以 B 的 MAC 地址为目的地址的链路层帧，帧包含 A 到 B 的 IP 数据报
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
6.4 局域网

## Slide 68: 寻址: 路由到另一 LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
  R 转发 IP 源 A，目标 B 的数据报
  R 创建以 B 的 MAC 地址为目的地址的链路层帧，帧包含 A 到 B 的 IP 数据报
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
6.4 局域网

## Slide 69: 寻址: 路由到另一 LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
  R 转发 IP 源 A，目标 B 的数据报
  R 创建以 B 的 MAC 地址为目的地址的链路层帧，帧包含 A 到 B 的 IP 数据报
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
6.4 局域网

## Slide 70: Homework
第6章后作业选做2题
测试腾讯会议准备考试环境
链路层与局域网

## Slide 71: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
  寻址、ARP
  以太网
  交换机
  VLAN
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 72: Ethernet
"dominant" wired LAN technology:
single chip, multiple speeds (e.g., Broadcom BCM5761)
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe's Ethernet sketch
6.4 局域网
Notes: https://blog.csdn.net/weixin_42229404/article/details/81227377

## Slide 73: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
star: prevails today
  active switch in center
  each "spoke" runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
bus: coaxial cable
star
6.4 局域网

## Slide 74: Ethernet frame structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type
6.4 局域网

## Slide 75: Ethernet frame structure (more)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type
6.4 局域网

## Slide 76: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet's MAC protocol: unslotted CSMA/CD with binary backoff
6.4 局域网

## Slide 77: 802.3 Ethernet standards: link & physical layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer
6.4 局域网

## Slide 78
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 局域网
    addressing, ARP
    Ethernet
    switches
    VLAN
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request
第六章 链路层和局域网
The 链路层和局域网

## Slide 79: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
  寻址、ARP
  以太网
  交换机
  VLAN
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 80: Ethernet switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame's MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured
6.4 局域网

## Slide 81: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A' and B-to-B' can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A'
B
B'
C
C'
1
2
3
4
5
6
6.4 局域网

## Slide 82: Switch forwarding table
Q: how does switch know A' reachable via interface 4, B' reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A'
B
B'
C
C'
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
6.4 局域网

## Slide 83: Switch: self-learning
A
A'
B
B'
C
C'
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch "learns" location of sender: incoming LAN segment
  records sender/location pair in switch table
A A'
Source: A
Dest: A'
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
6.4 局域网

## Slide 84: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */
6.4 局域网

## Slide 85: Self-learning, forwarding: example
A
A'
B
B'
C
C'
1
2
3
4
5
6
frame destination, A', location unknown:
A A'
Source: A
Dest: A'
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A'
A A'
A A'
A A'
A A'
flood
A' A
destination A location known:
A'
4
60
selectively send
on just one link
6.4 局域网

## Slide 86: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
6.4 局域网

## Slide 87: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
6.4 局域网

## Slide 88: Institutional network
to external
network
router
IP subnet
mail server
web server
6.4 局域网

## Slide 89: Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
6.4 局域网

## Slide 90: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
  寻址、ARP
  以太网
  交换机
  VLAN
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 91: VLAN: motivation
consider:
CS user moves office to EE, but wants connect to CS switch?
single broadcast domain:
  all layer-2 broadcast traffic (ARP, DHCP, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues
Computer
Science
Electrical
Engineering
Computer
Engineering
6.4 局域网

## Slide 92: VLAN
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual 局域网over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches
6.4 局域网

## Slide 93: Port-based VLAN
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
dynamic membership: ports can be dynamically assigned among VLAN
router
forwarding between VLAN: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers
6.4 局域网

## Slide 94: VLANspanning multiple switches
trunk port: carries frames between VLANdefined over multiple physical switches
  frames forwarded within VLAN between switches can't be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1
6.4 局域网
Notes: In information technology, vanilla (pronounced vah-NIHL-uh ) is an adjective meaning plain or basic. The unfeatured version of a product is sometimes referred to as the vanilla version. The term is based on the fact that vanilla is the most popular or at least the most commonly served flavor of ice cream. Or, as Eric Raymond, editor of The New Hacker's Dictionary , puts it, the default ice cream.
IBM's BookMaster product, a text publishing system used in mainframe environments, provides a default way, called vanilla , to specify which parts of the book to publish, and another fancier way to specify it, called mocha .
Some Web sites with frames call the simpler version of their site the vanilla version.

## Slide 95
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q VLAN frame format
802.1 frame
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type
6.4 局域网
Notes: ToS: Terms of Service

## Slide 96: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 97: Multiprotocol label switching (MPLS)
initial goal: high-speed IP forwarding using fixed length label (instead of IP address)
  fast lookup using fixed length identifier (rather than shortest prefix matching)
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
S
TTL
20
3
1
5
6.5 link virtualization: MPLS

## Slide 98: MPLS capable routers
a.k.a. label-switched router
forward packets to outgoing interface based only on label value (don't inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
flexibility: MPLS forwarding decisions can differ from those of IP
  use destination and source addresses to route flows to same destination differently (traffic engineering)
  re-route flows quickly if link fails: pre-computed backup paths (useful for VoIP)
6.5 link virtualization: MPLS

## Slide 99: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
IP routing: path to destination determined by destination address alone
R4
6.5 link virtualization: MPLS

## Slide 100: MPLS versus IP paths
R2
D
R3
R4
R5
A
R6
IP-only
router
IP routing: path to destination determined by destination address alone
MPLS and
IP router
MPLS routing: path to destination can be based on source and destination address
  fast reroute: precompute backup routes in case of link failure
entry router (R4) can use different MPLS routes to A based, e.g., on source address
6.5 link virtualization: MPLS

## Slide 101: MPLS signaling
modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing,
  e.g., link bandwidth, amount of "reserved" link bandwidth
D
R4
R5
A
R6
entry MPLS router uses RSVP-TE signaling protocol to set up MPLS forwarding at downstream routers
modified
link state
flooding
RSVP-TE
6.5 link virtualization: MPLS

## Slide 102: MPLS forwarding tables
R1
R2
D
R3
R4
R5
0
1
0
0
A
R6
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
10 A 0
12 D 0
1
in out out
label label dest interface
8 6 A 0
0
8 A 1
6.5 link virtualization: MPLS

## Slide 103: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 104: Data center networks
10's to 100's of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container,
Chicago data center
6.6 data center networking

## Slide 105
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
Load
balancer
Load
balancer
B
1
2
3
4
5
6
7
8
A
C
Border router
Access router
Data center networks
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)
Internet
6.6 data center networking
Notes: TOR(Top of Rack): 机架顶部
blade: 刀片机

## Slide 106
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Data center networks
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy
6.6 data center networking

## Slide 107: 第六章 链路层和局域网
6.1 概述、服务
6.2 差错检测、纠正
6.3 多路访问协议
6.4 局域网
6.5 链路虚拟化: MPLS
6.6 数据中心网络
6.7 网上浮生一日：web 请求的历程
链路层与局域网

## Slide 108: Synthesis: a day in the life of a web request
journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com
6.7 a day in the life of a web request

## Slide 109: A day in the life: scenario
Comcast network
68.80.0.0/13
Google's network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser
6.7 a day in the life of a web request

## Slide 110: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
6.7 a day in the life of a web request

## Slide 111: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client's IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply
6.7 a day in the life of a web request

## Slide 112: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply
6.7 a day in the life of a web request

## Slide 113: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
6.7 a day in the life of a web request

## Slide 114: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)
6.7 a day in the life of a web request

## Slide 115: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
6.7 a day in the life of a web request

## Slide 116: 第六章: summary
principles behind data 链路层 services:
  error detection, correction
  sharing a broadcast channel: multiple access
  链路层 addressing
instantiation and implementation of various 链路层 technologies
  Ethernet
  switched 局域网, VLAN
  virtualized networks as a 链路层: MPLS
synthesis: a day in the life of a web request
链路层与局域网

## Slide 117: 第六章: let's take a breath
journey down protocol stack complete (except PHY)
solid understanding of networking principles, practice
….. could stop here …. but lots of interesting topics!
  wireless
  multimedia
  security
链路层与局域网

## Slide 118: Homework
第6章后作业选做3题
链路层与局域网